## Slide 1: Bad Actor Analysis
Proactive Threat Management Engineering
PTM
Gbaran AGC1, AGC2; Otumara GTC

## Slide 2: Gbaran AGC1 Bad Actors
Chart: 
| Auto drain valve | Surge detected | UCP HMI frozen | GG overspeed | Radial bearing vibration | Pressurized trip from SIS | Resistance Temp. Device (RTD) | Comp. low lube oil (upon restart)
Sum of DownTime (Hrs) | 47.51 | 34.36 | 31.73 | 28.89 | 28.47 | 27.95 | 8.05 | 4.8
Count of Common description | 2 | 20 | 5 | 17 | 8 | 6 | 1 | 1
Sum of DownTime (Hrs)2 | 0.22436 | 0.38662 | 0.53646 | 0.67288 | 0.80733 | 0.93932 | 0.97733 | 1

## Slide 3: Insights – 80% Downtime Failures
Auto Drain Valve failure to close occurred twice, however MTTR = 23.75Hrs
Surge detected due to Choke issues on AGC1 amounting from anti-surge valve fault.
  Under CCC investigation.
UCP HMI Frozen
GG Overspeed module sends in faulty overspeed signals to trip the unit
  GG overspeed module now on site. Should be installed during Turn Around Mtce ongoing
Shaft radial bearing vibration fault

## Slide 4: Gbaran AGC2 Bad Actors
Chart: 
| Blow down valve | Turbine enclosure air flow | Bearing temperature | High HP seal gas flow - transmitter termination issue | Trip due throughput adjustment for AGC1 startup | F&G system device failure
Sum of DownTime (Hrs) | 20.37 | 13.4 | 9.17 | 6.42 | 1.05 | 1.03
Count of Events | 1 | 2 | 1 | 1 | 1 | 1
Sum of DownTime (Hrs)2 | 0.396 | 0.65649 | 0.83476 | 0.95956 | 0.97998 | 1

## Slide 5: Insights – 80% Downtime Failures
Blow down valve occurred “once” but had a downtime of 20Hrs
Turbine enclosure air flow switch occurred “twice”
Bearing temperature alarm occurred “once”

## Slide 6: Otumara GTC Bad Actors
Chart: 
| Joule-Thompson valve signal fault | Stg1-Scrubber vent valve (CMD disagree) | Stg4-Low dischrge pressure | FSV limit switch | HPC DE Seal Gas Press. Transmitter | Air filter DP | Stg3-Hi dischrge pressure | Stg4-Anti-surge valve (DVC)
Sum of DownTime (Hrs) | 39.24 | 18.72 | 17.7 | 5.46 | 3.66 | 1.42 | 0.83 | 0.52
Count of Events | 8 | 13 | 12 | 5 | 2 | 1 | 1 | 1
Sum of DownTime (Hrs)2 | 0.4482 | 0.66202 | 0.86419 | 0.92656 | 0.96836 | 0.98458 | 0.99406 | 1

## Slide 7: Insights – 80% Downtime Failures
Joule-Thompson valve drops pressure from HP (12 Bar) to LP (3 Bar)
  It experienced signal faults and tripped the Compressor
Stage 1 Scrubber vent valve Command disagree – Does not respond appropriately to command signals
Stage 4 Low discharge pressure trip

## Slide 9: Reliability (AGC1)
Chart: 
| 43831 | 43862 | 43891 | 43922 | 43952 | 43983 | 44013 | 44044 | 44075 | 44105
Reliability (%) | 94.41 | 90.25 | 97.9 | 93.38 | 98.98 | 99.09 | 99.1 | 96.14 | 96.36 | 85.88
Availability (%) | 94.41 | 90.25 | 97.9 | 93.38 | 98.98 | 99.09 | 99.1 | 96.14 | 96.36 | 85.88
Utilization (%) | 94.41 | 90.25 | 97.9 | 93.38 | 97.99 | 97.3 | 99.1 | 96.14 | 95.66 | 85.88

## Slide 10: Reliability (AGC2)
Chart: 
| 43831 | 43862 | 43891 | 43922 | 43952 | 43983 | 44013 | 44044 | 44075 | 44105
Reliability (%) | 97.12 | 99.81 | 98.77 | 100 | 97.8 | 100 | 100 | 97.26 | 99.18 | 100
Availability (%) | 97.12 | 99.81 | 98.77 | 100 | 82.73 | 100 | 100 | 97.26 | 98.29 | 100
Utilization (%) | 97.12 | 99.81 | 93.32 | 87.57 | 82.73 | 100 | 100 | 97.26 | 98.29 | 100

## Slide 11: Reliability (Otumara GTC)
Chart: 
| 43831 | 43862 | 43891 | 43922 | 43952 | 43983 | 44013 | 44044 | 44075 | 44105
Reliability (%) | 98.62 | 98.13 | 99.48 | 99.73 | 98.58 | 99.43 | 98.77 | 96.08 | 96.05 | 100
Availability (%) | 98.62 | 98.13 | 99.48 | 99.73 | 98.58 | 88.14 | 98.65 | 95.86 | 76.16 | 100
Utilization (%) | 70.99 | 98.13 | 99.48 | 99.73 | 98.58 | 79.72 | 92.73 | 95.86 | 75.99 | 100