## Slide 1: 2018 Okoloma PU Delivery Strategy Workshop
Syndicate Report Back

## Slide 2: PRODUCTION ENHANCEMENT SYNDICATE REPORT OUT
 | Opportunities | Reward |  | Challenges | Recommendation/Improvement Plan | Action Party
 | Potential | Oil kbopd | Gas MMscf |  |  | 
1 | Current gas potential of 204 MMscf/d not sure of the dryness to wetness factor |  | 204 | Lack of assurance on volumes* Sampling points at 12 o’clok position instead of 3 or 9 o’clock position | * Re-engineer sampling points Confirm actual dry gas potential through MRT for all gas wells | Asset Engr WRFM/Ops
2 | AFAM 26 Availability |  | 40 | *Not sure of the terms and conditions for producing the well | Confirm terms and conditions for producing the well. Acquire current production data trend, model and engage DPR for a revised permit to produce well based on current operating parameters | WRFM/FMT/OPS
3 | Afam 27 |  | 25 | * Not sure of the terms and conditions to switch the well to the gas leg | Confirm terms and conditions for producing the well. Acquire current production data trend, model and engage DPR for a revised permit to produce well based on current operating parameters | WRFM/FMT/OPS
4 | Afam 15 |  | 5 | A closed in NAG requires hydraulic workover to install velocity string and produce Funding as it was dropped out of AF basket | Funding for gas opportunity Cost estimate Workover candidate/proposal | AMIL CWI WRFM/FMT
5 | New gas wells ( 2 nos) |  | 100 | Planned for 2035 | Decision to fastrack maturation and fund earliest | HDM
 | Total |  | 370 |  |  | 

## Slide 3: PRODUCTION ENHANCEMENT SYNDICATE REPORT OUT
 | Opportunities | Reward |  | Challenges | Recommendation/Improvement Plan | Action Party
 | Potential | Oil kbopd | Gas MMscf |  |  | 
1 | Existing oil | 2 |  |  |  | 
2 | Existing condensate based of gas of 204 MMscf/d | 14 |  | Funding | Funding for STOG Data acquisition/evaluation for execution | AMIL WRFM/FMT CWI
3. | Additional Condensate from additional gas of ca 40 MMscf/d | 3 |  |  | MRT post restorations | OPS/WRFM/FMT
4. | Bean up for Afam 25 & 27 | 0.5 |  | Confirmatory MER DPR Allowable | Conduct MER Obtain DPR allowable | Ops WRFM/FMT
5. | CIWRS (Afam 13, 16, 17 &19) | 1.75 |  | Funding | Funding for STOG Data acquisition/evaluation for execution | AMIL WRFM/FMT CWI
 | Total | 21.25 |  |  |  | 

## Slide 4: PRODUCTION ENHANCEMENT SYNDICATE REPORT OUT
 | Opportunities | Reward |  | Challenges | Recommendation/Improvement Plan | Action Party
 | Facility (Haulage/Capacity) | Oil kbopd | Gas MMscf |  |  | 
1 | Existing facility limit gas (combined mode) |  | 240 |  |  | 
2 | Opportunity to debottleneck plant and unlock 30 mmscf/d additional to take plant to 270 MMscf/d |  | 30 | Major plant re-engineering | Long term option based on gas customers availability from commercial versus current demand for 280 Mmscf/d from both primary and secondary customers Opportunity for backfeed from Interfeed line to NGC (40 mmscf/d) | AMIL Gas commercial Agbada/Obigbo/Imoriver PUs
 | TOTAL |  | 240 + 40 (INTERFIELD) |  |  | 
3 | Existing facility limit Oil (combined mode) | 30 |  |  |  | 
4. | Opportunity for new oil well to for full capacity utilization of ca 8.75 Mbopd on top the total estimated liquid potential of 21.25 Mbopd | 8.75 |  | No new oil well planned for Okoloma in the near future | Explore opportunity for oil well | Dev
5 | XXHP Commissioning |  |  | Facility yet to be commissioned | Commission and handover facility | Project Team
 | Total | 30 |  |  |  | 

## Slide 5: PRODUCTION ENHANCEMENT SYNDICATE REPORT OUT
 | Opportunities | Reward |  | Challenges | Recommendation/Improvement Plan | Action Party
 | Availability (Wells, flowlines & facilities + SP) | Oil kbopd | Gas MMscf |  |  | 
1 | Pneumatic pump to open up wells post trip |  |  | Over reliance on CWI for routine well o/u post trips | Evaluate current proposal from Ops and procure hand pump for routine interventions | AMIL/WI
2 | Sustaining minimum flow for all wells as per operating envelope |  |  | Wells quitting resulting in reduced availability to meet gas demand | RE ‘s and Process Engr ro study and advise | PE FMT
3 | FGC compressor availability |  |  | Overdue major inspection | Execute inspection asap | AGG Improvement Team
 | Export pumps availability |  |  | Turn around time from breakdown | Critical spares stocking Mtce team to eveluate the maintenance strategy on pumps | mtce
 | Increase uptime of facilities during TNP Outages |  |  | Combined shutdowns affecting other facilities not related to the delivery line | Install isolation valves at Kom-kom manifold | Aset Engr Process Engr
 | Control unit fro GRF in Afam V |  |  |  | Relocate control unit to GRF | Asset Engr
 | Expedite PO creation for spares & materials availability |  |  | Extended delivery time as compared to ROS dates and MTTR PO creation time Strategy for critical spares availability | STA for Asset Reps to C&P for enhanced awareness on process PU dedicated CP Specialist Bring back price agreements on stock items SLAs between Asset & CP | AMIL

## Slide 6: COST IMPROVEMENT FOR 2018 SYNDICATE REPORT OUT
 | Opportunities | Reward |  | Challenges | Recommendation/Improvement Plan | Action Party
 | Direct Costs | Oil kbopd | Gas MMscf |  |  | 
1 | Production Operations: |  |  | High cost as all Operations and Maintenance support personnel salaries are captured under Facility Operations account | Optimise Operations and Maintenance support personnel in Ebenezer Project | AMIL/ PUMs
2 | Condensate Export Pumps |  |  | Frequent mech seal failure Spares Overhauls Fit for purpose verification | Pump Overhaul contractor to liaise with OEM representative to secure the right spares for pump overhaul to provide a lasting solution and improve pump performance to achieve cost saving | Collins Iyoloma
3 | DIY |  |  | Metering monthly schedule 6M Valve greasing Wellhead open up by CWI Team | Form Corporate DIY team for LAND East Asset; train personnel and procure equipment for activity execution. | OZ
4 | Charge back on associated costs |  |  | Improper review of monthly Transaction listing | Carry out monthly cascade of PU Financial performance/ transaction listing | Wale/ Ebere/Lizy
5 | Catering cost Reduction |  |  | Feeding of unauthorize personnel in the facility | Implement e-meal ticketing project ASAP | Roland/ Chioma
6 | Logistics chargeback monitoring |  |  | Most times Logistics will not provide the right ton of equipment required for an activity and force Asset to pay extra for their lapses | Monitor charge back based on agreed services | Ebere/Erons/ Lizy
7 | Review breakdown of cost of Maintenance services |  |  |  | Review cost breakdown for all Maintenance contract services to eliminate double dipping | Soba/ Rume

## Slide 7: COST IMPROVEMENT FOR 2018 SYNDICATE REPORT OUT
 | Opportunities | Reward |  | Challenges | Recommendation/Improvement Plan | Action Party
 | Direct Costs | Oil kbopd | Gas MMscf |  |  | 
8 | Paper Cost Reduction: |  |  | Printing of work pack for all PM & CM activities are very cumbersome | Standardise one off work pack to achieve paper reduction project | Soba/ Rume
9 | Imprest Account |  |  | Delay in operations as a result of impress account | Provide impress account to achieve smooth operation and eliminate unnecessary downtime | AM

## Slide 8: HSE AND PEOPLE SYNDICATE REPORT OUT
 | Opportunities | Reward |  | Challenges | Recommendation/Improvement Plan | Action Party
 | Potential | Oil kbopd | Gas MMscf |  |  | 
1 | Achieve goal zero in all facilities operated by Okoloma PU |  |  | Bad Roads | Apply continuous Risk Assessment on Land Transport by Journey Management team Engage Government Relations on future plans | Journey Mgr External Relations
2 | Achieve goal zero in all facilities operated by Okoloma PU |  |  | Security | Compliance to complimentary escort with respect to SOL as spelt out in the policy. | ASA
3 | Achieve goal zero in all facilities operated by Okoloma PU |  |  | PPE Availability and quality | Tie in to SE PPE Improvement project Apply consequence management to non-compliance and institute reward scheme for individual high performance in HSE Conduct PPE audit regularly | Asset SE Adviser PUM Asset SE Adviser
4 | Achieve high level of Service delivery |  |  | Accommodation + Catering + Services | Enhance manning level planning vs activity Enforce quality service delivery from all Contractors. Localize Task and Targets of all Company/Contractor reps and integrate with SE team. Enhance and energize the Welfare team | PUM PUM/Contract Holder PUM/Contract Holder PU
5 | Meet up target for flare and avoid fines associated with flaring |  |  | Flare | Cross check Flare target and associated assumptions Complete GHG Plan for the PU | PUM
6 | Sustained production without interruption |  |  | Obsolescence management | Progress implementation of recommendation of the ORAT tool used for the risk assessment. | PUM/MTL

## Slide 9: HSE AND PEOPLE SYNDICATE REPORT OUT
 | Opportunities | Reward |  | Challenges | Recommendation/Improvement Plan | Action Party
 | Potential | Oil kbopd | Gas MMscf |  |  | 
1 | Motivation and increased productivity |  |  | Rewards and Recognition | Develop framework for the PU Review applicable contracts to include a % line item for performance reward | PU Contract Holder
2 | Capacity building |  |  | Training vis a vis work schedule | Develop effective localised procedure to manage nominations. | PUM/TLs
3. | Career development |  |  | CN stagnation | Encourage family unit model and encourage exploring outside opportunities that could also refresh the PU | PU
4 | Improved Infrastructure |  |  | Unavailability of visitors toilets Slow Wi-Fi in Accommodation areas | Explore options and make toilets available. Obtain DPR allowable | AMIL IT Support
5. | Manning |  |  | Absence management | Upskill Contract staff competence to stand- in | PU
6. | Appraisal |  |  | Appraisal + Feedback | Deliberate effort by supervisors and sub-ordinates to do appraisal and feedback quarterly in a structured manner | PU

## Slide 10: HSE AND PEOPLE SYNDICATE REPORT OUT
 | Opportunities | Reward |  | Challenges | Recommendation/Improvement Plan | Action Party
 | Potential | Oil kbopd | Gas MMscf |  |  | 
1 | Motivation |  |  | Delayed Salary Payments | Ensure timely payments by Contracts Holders executing their Roles and Responsibilities adequately. Effective escalation and seek waiver 3 months prior to expiration of contracts. Contract Holders to track expiration of contracts effectively. | Contract Holders
2 | Unscheduled Facility Audits |  |  | Disruption to daily operations | Proactive engagement of PU before the audits | SE LEH
. |  |  |  |  |  |