## Slide 1: Eliminate Gbaran exposure of USD20mln in 2024 on BS&W measurement noncompliance
Fit4 ID
Workstream | Opex
Location(s) | SPDC Production asset
Current L-Gate | L0 | Initiative Lead | XXXX
L1 Date | DD MMM YYYY | Initiative Sponsor | XXXXX
L2 Date | DD MMM YYYY |  | 
Problem Statement
Between January and May 2023, Gbaran incurred excess water uplift loss/penalty equivalent to 144kbbl Net oil due to use of non approved method in determining crude production BS&W. This translated to actual revenue loss of USD10.8mln. The Regulation requires that Dynamic metering system for custody transfer and allocation shall be designed based on LACT (equipped with pipe prover and automatic sampling unit). Auto sampler remains the only approved device for BS&W measurement. Gbaran has dynamic metering system that is not in line with LACTs design. However, BS&W for export is currently determined by Agar online watercut meter and manual sampling method and incurs penalty for non-compliance of not having approved auto sampler for BS&W measurement. If auto sampler is not installed we will continue to incur this losses pending completion of the LACT project in 2025.
Initiative Description
This initiative seeks to mitigate the significant value erosion from penalties by fast-tracking the installation of fit-for-purpose automatic sampling system to determine BS&W at Gbaran. Installation of auto sampler will deliver the following benefits. Mitigate excess water uplift loss/penalty equivalent to ca. 5 – 20% of Net Oil monthly. Compliance with regulatory requirement for water measurement. Accurate determination of BS&W for production optimization.
Estimate Impact
USD20mln value protection on losses due to excess water uplift for 2024 based on actual loss of 10.8mln from Jan – May 2023.
Key Stakeholders
Project Sponsor: John Fraeijhoven Implementation Lead: Samson Uzoka,. Project Team: Babs Alepaye, Chibuzo Onumadu, Godfrey Omokaro, Othuke Okpokoro, Iki Dienagha etc.
Decisions needed to mature
Formal agreement and alignment with NUIMS for Budget provision. Alignment with Regulators (NUPRC)
What does success look like at the end of the Sprint
Achieve successful installation and commissioning by August 2024. Regulator’s approval of the autosampler after SAT completion. No more application of water uplift for all measurement at Gbaran.