## Slide 1
  Business Unit: Waste Management
  Project Sponsor: Victor Ojabo
  Champion: Stephen Iheozor
PROJECT OWNERSHIP
This will make it possible to reduce the quantity of hazardous waste sent to third party incinerators and landfill translating into cost savings and reduced waste footprint.
OPPORTUNITY STATEMENT
IN:
Build the required waste holding bay that would enable
Procure additional tools (Trolleys, Shovels, Buckets, rakes, baskets etc.)
adjust the Operating hours of the plant from 8 hours to 16 hours
SCOPE
The Shell General Waste Incinerator was installed in August 2003 to replace an open burner, which was formerly being used to handle Medical Wastes at IA. It was dedicated to incineration of medical wastes like syringes, human tissues, bottles and laboratory wares. The capacity of the incinerator is 250kg/hr. Currently, it treats between 11 tones per annuum. An MoC number 53983 approved in October 2018 for the Incinerator to start burning other waste streams apart from medical wastes, including Contaminated paper/cartons, Oily Rags/Adsorbents, Municipal Solid Waste (MSW) and Sewage cake. However due to absence of on-site holding capacity for these waste at the Incinerator and the limited working hours of the plant, this opportunity has not been fully utilized. This Charter is to undertake Project to ensure the full utilization of the incinerator’s capacity.
BUSINESS CASE
Project Title: (OPTIMISATION OF THE GENERAL WASTE INCINERATOR, Shell I.A. Port Harcourt)
  Team Members:
  TERVER Atsar
  Dickson Abanum
  Vivien Idioma
  Adulphus Osuya
  Boye Famoroti
To increase the capacity utilization; increase quantity of waste incinerated at the incinerator from 11tonnes to 20 tones per year (Solid Hazardous Wastes -Oily rags, oil impacted vegetation; Solid Non-hazardous Wastes - Garbage, Floaters, Cartons, Confidential documents).
To reduce use of third Party Incinerators
GOAL
Budget Availability
Equipment Integrity
POTENTIAL ROADBLOCKS/ ISSUES
OUT:
Incineration of some waste steams - Liquid Wastes(chemicals/paints); Plastics; Glass; Tonner Cartridges/Filters; Used Oil/Lubes
Gross Hard Benefits*:
Soft Benefits:
BENEFITS
PROJECT STATUS
G
Y
R
On Track
Delayed
Stopped
0%
0%
50%
Health
% Comply
Completion Date
Start Date
Overall % Comply
0%
IDENTIFY
IMPROVE
SUSTAIN
G
0%
CLOSE
NS
Not Started
NS
F$500,000 savings per Annum
Minimize waste footprint
NS
NS