## Slide 1: Optimise Aircraft fleet from 5 to 4 to meet SCiN demand by November 2021
L4 date
Initiative lead
David Cameron
Current stage gate
L2
Initiative sponsor
Victor Ojabo/Paul Van Den Hemel
L5 date
December 2021
November 2021
Problem statement
  Context: current demand for air transportation is met with 5 aircraft broadly assigned to bases (1x Warri, 2x PHC, 2x Lagos). Historic utilisation of the aircraft flying capacity is trending at ~67%, consistent across bases. Seat utilisation was trending around 85% (40% last 7 months)
  Complications:
  Local supplier (Caverton Helicopters) profitability which might be significantly impacted
  Uncertainty of future demand outlook given COVID-19 and OPEC production cuts
Initiative description
  Reduce aircraft fleet from 5 to 4 while meeting SCiN demand and not compromising on safety
Estimate impact
24162
Wave ID
Location(s)
SCiN
Workstream
Opex
Key stakeholders
Implementation plan: key actions required
Risks:
  Assumption: 4 aircraft by November 1st, 2021
  Savings: $3.97 million per annum saving on elimination of Monthly Standing Charge element; total flying hours assumed to remain the same (redistributed between remaining 4 aircraft resulting in higher capacity utilisation) Additional positioning flights will reduce this to US$ 3.65 million per annum.
  GM/DMD; MD SNEPCo; PS Mgr
  Asset Mgrs
  GM Wells
  GM C&P
  SPDC FD/ SNEPCo FD
  NAPIMS / NCDMB
  Caverton Helicopters
  Commercial:
  Develop vendor engagement strategy (BATNA)
  Engage the vendor to agree operating model with 4 aircraft
  Release the note to the vendor + 90 days notification period
  Decreased service levels due to less spare capacity if demand surges (e.g., spike in the activities post-COVID, increased emergency response requirements, etc.)
  Risk of vendor increasing rates for remaining services if they are unable to breakeven (mitigation: development of negotiation strategy as part of the implementation plan)
  Process:
  “Demand on paper” exercise to identify required changes to demand management Incorporate changes to e2d LMS
  Syndicate with key stakeholders
  Operate based on revised process

## Slide 2: Jan – Apr 2021 Demand vs Capacity Profile – 4 helis (28/28 Rota)
WK 1 - 17 Actual Pax Demand Average based on 6D per week
3 Rigs
All FLBs
Bonga
EA
Projects
Pipelines
DS10
FYIP
ERT
BOGT/FOT – Via Twin Otter
121
841
Chart: AIRCRAFT UTILIZATION WK 1 - 17
| Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | WK 1 | WK 2 | WK 3 | WK 4 | WK 5 | WK 6 | WK 7 | WK 8 | WK 9 | WK 10 | WK 11 | WK 12 | WK 13 | WK 14 | WK 15 | WK 16 | WK 17 | 10-Jan | 17-Jan | 24-Jan | 31-Jan | 7-Feb | 14-Feb | 21-Feb | 28-Feb | 7-Mar | 14-Mar | 21-Mar | 28-Mar | 4-Apr | 11-Apr | 18-Apr | 25-Apr | 2-May
PHC | 466 | 414 | 425 | 368 | 486 | 312 | 433 | 424 | 453 | 359 | 458 | 348 | 351 | 280 | 412 | 311 | 451 | 388 | 372 | 272 | 423 | 311 | 461 | 382 | 408 | 339 | 348 | 257 | 347 | 343 | 365 | 337 | 440 | 355
WARRI | 298 | 239 | 322 | 280 | 335 | 283 | 586 | 516 | 420 | 202 | 377 | 332 | 326 | 260 | 519 | 405 | 361 | 266 | 351 | 288 | 406 | 339 | 546 | 487 | 396 | 286 | 310 | 269 | 456 | 331 | 519 | 441 | 374 | 310
LAGOS | 181 | 175 | 156 | 152 | 128 | 106 | 170 | 157 | 172 | 200 | 168 | 177 | 119 | 120 | 168 | 139 | 216 | 196 | 186 | 197 | 264 | 166 | 201 | 166 | 227 | 179 | 215 | 212 | 237 | 217 | 159 | 170 | 251 | 231
Total Capacity | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160
Actual Capacity | 1640 | 1640 | 1640 | 1440 | 1440 | 1440 | 1340 | 1340 | 1340 | 1800 | 1800 | 1800 | 1560 | 1560 | 1560 | 1620 | 1620 | 1620 | 1260 | 1260 | 1260 | 1480 | 1480 | 1480 | 1560 | 1560 | 1560 | 1380 | 1380 | 1380 | 1580 | 1580 | 1580 | 1740 | 1740 | 1740 | 1540 | 1540 | 1540 | 1360 | 1360 | 1360 | 1660 | 1660 | 1660 | 1640 | 1640 | 1640 | 1660 | 1660
RW seat utilization is 39%
RW demand credibility is 83%
FW demand credibility is 80%
 | RW Seat Utilization | Demand Credibility
PHC | 36% | 82%
WARRI | 39% | 80%
LOS | 49% | 92%
 | Airframe | Max Daily Flight per Airframe | Effective airframe seat capacity
PHC | 2 | 4 | 10
WARRI | 1 | 7 | 10
LOS | 1 | 3 | 10

## Slide 3: Q4 2020 Demand vs Capacity Profile – 4 helis (28/28 Rota)
WK 40 - 53 Actual Pax Demand Average based on 6D per week
3 Rigs
All FLBs
Bonga
EA
Projects
Pipelines
DS10
FYIP
ERT
BOGT/FOT – Via Twin Otter
93
853
Chart: AIRCRAFT UTILIZATION WK 40 - 53
| Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | Planned Pax | Actual Pax | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 4-Oct | 11-Oct | 18-Oct | 25-Oct | 1-Nov | 8-Nov | 15-Nov | 22-Nov | 29-Nov | 6-Dec | 13-Dec | 20-Dec | 27-Dec | 3-Jan
PHC | 513 | 338 | 429 | 339 | 563 | 410 | 264 | 181 | 380 | 348 | 629 | 439 | 522 | 362 | 420 | 369 | 381 | 314 | 424 | 376 | 600 | 378 | 559 | 468 | 335 | 284 | 314 | 279
WARRI | 343 | 313 | 637 | 484 | 455 | 321 | 306 | 148 | 420 | 304 | 806 | 670 | 495 | 370 | 387 | 304 | 427 | 314 | 484 | 394 | 544 | 449 | 411 | 314 | 350 | 297 | 448 | 360
LAGOS | 138 | 140 | 143 | 123 | 195 | 164 | 120 | 111 | 119 | 122 | 144 | 145 | 196 | 187 | 152 | 139 | 168 | 152 | 128 | 133 | 239 | 219 | 179 | 168 | 99 | 106 | 110 | 111
Total Capacity | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160 | 2160
Actual Capacity | 1600 | 1600 | 1600 | 1640 | 1640 | 1640 | 1680 | 1680 | 1680 | 660 | 660 | 660 | 1440 | 1440 | 1440 | 1880 | 1880 | 1880 | 1920 | 1920 | 1920 | 1580 | 1580 | 1580 | 1700 | 1700 | 1700 | 1700 | 1700 | 1700 | 1640 | 1640 | 1640 | 1720 | 1720 | 1720 | 1380 | 1380 | 1380 | 1280 | 1280

RW seat utilization is 40%
RW demand credibility is 80%
FW demand credibility is 76%
 | RW Seat Utilization | Demand Credibility
PHC | 36% | 77%
WARRI | 43% | 77%
LOS | 40% | 95%

## Slide 4: Capacity calculations and assumptions used
As per the data used for simulation modelling, we observed the following :
Even on very busy days it is possible to reach ~64% flying hours from Lagos, ~61% flying hours from Port Harcourt and 52% Flying hours from Warri based on 10.5 available hours and Flying from 8:00 to 18:30
In addition, the average number of flying hours, and average number of flights per week is available for each helibase from the historical data used, see below
NOTE : The term Flight here refers to a round-trip (not one way journey)
It is assumed that the following aircraft are available as a start
    2 x helicopters at Lagos
    2 x helicopters at PH
    1 x helicopter at Warri.
  It is assumed that each aircraft can carry 10 PAX on average
From the data and assumptions on the left average capacity can be estimated as below (as an example for Lagos):
A = Average no of flying hours available at Lagos = available hours * No. of aircraft * average actual flying hours from history = 10.5*2*64% (see point 1 on left) = 13.44
B = Flying time per flight (Round trip) = total flying hours / Nr. Of Flights = 63.4/26 (from table under point 2 alongside) = 2.46
Average no of round trips / day = A/B = 5.46
Assuming 10 PAX per flight ,total PAX capacity = 5.46x10 = 55
This is further rationalised based on observations (see next slide)

## Slide 5: Capacity calculations - Continued
Following the approach explained, the average PAX capacity per base is calculated as below . Also, the estimated capacity with 4 Helicopters is calculated based on the assumption of 1 less heli at Lagos, and for 3 helicopters it is assumed that each helibase operates with 1 helicopter each.
NOTE :
The capacity shown is per round trip – therefore it can be assumed that the same capacity is available outbound and inbound, in other words –with 2 aircraft, 60 PAX can be flown outbound from Lagos on average, therefore 60 PAX can be flown inbound as well.
 |  |  |  |  |  | 5 heli | 4 heli | 3 heli
 | Available daily flying hours | Average flight duration | Average no. of round trips per day | Min Flights / day | Max flights / day | Rounded pax capacity (outbound or inbound) |  | 
L (2 heli) | 13.44 | 2.461538 | 5.46 | 4 | 6 | 60 | 30 | 30
PH (2 heli) | 9.81 | 1.4 | 7.007143 | 6 | 8 | 80 | 80 | 40
W (1 heli) | 5.46 | 0.665217 | 8.207843 | 5 | 7 | 70 | 70 | 70
Total |  |  |  |  |  | 210 | 180 | 140
3 hours have been reduced from available daily flying hours to account for overflights
Even though avg max flights calculated is 8, practically it is not considered realistic for 1 aircraft, therefore reduced to 7
Avg pax per flight = 10

## Slide 6: 5 key risks have been identified
Future demand above historic averages (e.g., spike in the activities post-COVID)
Emergency response requirements above base assumptions
Insufficient dedicated capacity to meet the demand with 1 airframe less for any base
Increased rates on remaining aircrafts if vendor is unable to breakeven with reduced scope of services
Contractual limitations for “capacity pooling” due to structure (2 contracts currently for 2+3 helicopters potentially assigned to certain bases)
Decreased service levels (inability to meet demand)
Value erosion
Theme
Risk
Mitigation measure
  Incorporate activity based long-term demand planning (vs operational 2 weeks outlook) into e2e LMS to improve demand visibility in the scheduling horizon, stabilise integrated work schedule and agree improved control of demand changes
  Buffer capacity to meet emergency requirements to be tested and clearly documented during “Demand on paper” exercise; active demand management to have clear action plan in case if demand cannot be met
  Adopt “capacity pooling” approach to demand planning (vs currently dedicated airframes approach)
  Leverage planned work off-shore (Work Orders) to smoothen peaks and troughs in demand for passenger movement
  Agree integrated logistics scheduling process with the business during stakeholder engagement sessions to ensure buy-in and collaboration
  Optimise demand further (routing optimisation, surveillance flights optimisation etc.) as part of business as usual activities
  Develop clear negotiation strategy incl. BATNA
  To be validated

## Slide 7: $3.65 Million annual savings can be achieved from November 2021
Chart: 
 | 222172 | 222172 | 347658.2466 | 347658.2466
 | 125486.2466 | 0
Monthly aircraft rent USD element
Additional positioning
USD
Total monthly savings
Monthly aircraft rent NGN element
26,000
  RW AW139 MSC rate per aircraft per month
  Assuming one aircraft per week positioning empty between Lagos and Port Harcourt.
Expected savings, $305,554 per month
  RW AW139 MSC rate per aircraft per month at 413 NGN/USD FX rate

## Slide 8: L3 implementation plan developed
today

## Slide 9: Additional risks that the studies do not consider
The current demand for PH and Warri (see week 12) could not be achieved with 2 aircraft between the two bases. Additionally, the plans do not include break-ins.
Aircraft unserviceability –Recently one AW139 was unserviceable for about two weeks, the programme was mostly achieved because there were still 4 AW139s to complete the flight schedules. If there were only 4 Aw139s to start with, the programme could not have been achieved with the remaining 3. There were periods in the past (end of 2019) where 3/4 aircraft were unserviceable or in scheduled maintenance.
There is little or no visibility of future demand, yes we lose 2 rigs soon, how many are coming on-hire that will have aviation demands (90 day notice to offhire, 120 days to rehire aircraft)?
There would be reduced ability to respond to company emergency requests, VIP flights, and any field re-entry requirements, e.g. Belema.
It is too simplistic to say that 28/28 reduces the demand because during the current period we are applying COVID controls, meaning the actual flight demand requires two flights per rotation for any group that would normally require one flight. i.e. The crew going to the field go in a week early and then their back-to-backs come out a week later once the replacements have been cleared to work.
When flight are required that cannot be met with the existing capacity and we need ad-hoc (from CHL) aircraft. They may not actually be available, as CHL may drop an airframe themselves, and when they are available, they are expensive – 13,000 USD/hr, eroding any potential savings.
Repositioning an empty aircraft from one base to support another is expensive and inefficient (no seat utilisation). For example, Warri has a single aircraft that also covers night medevac, rarely does a week pass without needing a support Aircraft from Lagos or PHC due to temporary unserviceability or maintenance.
Weather issues, when morning fog, rain, harmattan or passenger related issues (Access, HUET etc) delay the flight programme, the current aircraft fleet can usually make-up the schedule once flying resumes, this may not be the case with 1 less aircraft.
Caverton issues – Dropping one aircraft will mean staff cuts, reduced morale, reduced revenue, greater financial instability and SCiN would no longer be the primary customer for Caverton.
An aircraft reduction will probably increase the commercial pressure upon pilots, engineers and other staff at the expense of safety.
There is no current PH to Lagos Fixed-Wing contract since BHNL was dropped, Real Estate are working a potential contract with Arik or BHNL, the Twin Otter (or replacement AW139 have been used to make-up this gap).