## Slide 1
SOKU LPNAG SUCTION PRESSURE DROP
37 TO 33.7 BAR | ADDITIONAL 16MMSCFD
SEP 2024
SOKU, SPDC

## Slide 2: LPNAG SUCTION PRESSURE DERATING ADDITIONAL 16MMSCFD HEALTHY TURBINE AND COMPRESSOR
37 TO
33.7 bar
16 MMSCF
STABLE
PARAM.
Post test data review indicated room to increase the production by further opening W36 and 39 chokes.
Water Evacuation remains a challenge in bringing additional wells
TEST PROCEDURE
Decrease pressure from 37 bar to 33.7 bar in 0.5 bar steps.
Held each pressure for 2 hours and recorded parameters.
Ensured parameters stay within turbine and compressor specs.
HEALTHY PARAMETERS IN ALL THE STEPS
Temperature, pressure, speed, and vibration were all within specifications.
Auxiliary equipment (seal gas, lube oil, etc.) also met specifications.
UP BY 16MMSCF, PARAMETERS MET SPEC
Flow increased 133 to 149mmscf.
Compressor pressure: 82 to 85 bar (Trip: 110 bar).
Turbine EGT: 1,289 to 1,331°F (Trip: 1427°F).
Turbine RPM: 5,911 to 6,400 (Trip: 6500 RPM)
PARAMETER DESCRIPTION | Delta | Percentage | SP 33.7 | SP 37 (as found)
Set Point (21UIC802) | 3.30 |  | 33.7 | 37.00
Comp. Suction Pressure [Trip Point = 50barg] | - 3.27 | -9% | 34.70 | 37.97
Comp. Discharge Pressure [Trip Point = 110barg] | 2.40 | 3% | 85.13 | 82.73
Export Pressure Plant static (EGGS) [Trip Point = 95 barg] | 0.70 | 1% | 73.50 | 72.80
Export Pressure Plant static (GTS) [Trip Point = 96 barg] | 3.57 | 4% | 84.07 | 80.50
Comp. Suction Temp (degF) [Trip Point = 338F] | 0.02 | 0% | 103.17 | 103.15
Comp. Discharge Temp (degF) [Trip Point = 338F] | 31.12 | 13% | 264.75 | 233.63
Turbine Exhaust Temp (EGT) (degF) [Trip Point = 1427F] | 41.64 | 3% | 1,331.33 | 1,289.69
Compressor Suction Flow (MMSCF) [Trip Point = NA] | 16.33 | 12% | 149.33 | 133.00
Gas Heat Exchanger (Fin-Fan cooler) outlet Temp. [Trip Point = 122F] | 6.74 | 7% | 97.34 | 90.60
Anti-Surge Valve % Opening [Trip Point = ] | - 0.12 | - | 0.01 | 0.14
Vibration - Radial x-vibr. HP Compressor NDE [Trip Point = 69um pp] | 0.03 | 0% | 6.90 | 6.86
Vibration - Radial vibration HP Compressor DE [Trip Point = 69um pp] | 0.19 | 2% | 8.53 | 8.34
Vibration - Axial displacement HP compressor [Trip Point = -/=0.6mm] | 0.03 | 10% | 0.27 | 0.25
Bearing Temperature (Non-Drive End) [Trip Point = 248F] | 6.10 | 3% | 223.88 | 217.77
Thrust Bearing temperature [Trip Point = 248F] | 2.67 | 2% | 135.49 | 132.82
Driver (Gas Turbine) Speed [Trip Point = 6500 rpm] | 488.26 | 8% | 6,400.01 | 5,911.75
RAW Data